## Contents
- Query user for logfile
- Separate raw, bandpassed, and motion filtered data from scn structure
- Pull out the raw scans (if saved)
- Create the waterfall horizontal and vertical axes
% plotMrmRetLog.m
% This script prompts the user for a MRM-RET logfile, reads, parses, and
% produces a "waterfall plot" of the motion filtered scans and detection lists
% in the logfile
clear all; close all; clc %#ok<*CLALL>
## Query user for logfile
%dnm = '.'; fnm = 'MRM_002.csv';
[fnm,dnm] = uigetfile('*.csv');
fprintf('Reading logfile %s\n',fullfile(dnm,fnm));
[cfg,req,scn,det] = readMrmRetLog(fullfile(dnm,fnm));
Reading logfile C:\Users\austinsbrown\Dropbox\ee384\lab7\RetLog_002.csv
## Separate raw, bandpassed, and motion filtered data from scn structure
(only motion filtered is used)
## Pull out the raw scans (if saved)
rawscansI = find([scn.Nfilt] == 1);
rawscansV = reshape([scn(rawscansI).scn],[],length(rawscansI))';
% band-pass filtered scans
bpfscansI = find([scn.Nfilt] == 2);
bpfscansV = reshape([scn(bpfscansI).scn],[],length(bpfscansI))';
% motion filtered scans
mfscansI = find([scn.Nfilt] == 4);
mfscansV = reshape([scn(mfscansI).scn],[],length(mfscansI))';
## Create the waterfall horizontal and vertical axes
Tbin = 32/(512*1.024); % ns
T0 = 0; % ns
c = 0.29979; % m/ns
Rbin = c*(Tbin*(0:size(mfscansV,2)-1) - T0)/2; % Range Bins in meters

figure
plot(Rbin, rawscansV)
title('Raw Scan'), xlabel('Meters'), ylabel('Amplitude')

figure
plot(Rbin, bpfscansV)
title('Bandpass Values'), xlabel('Meters'), ylabel('Amplitude')

figure
plot(Rbin, mfscansV)
title('Motion Filtered Values'), xlabel('Meters'), ylabel('Amplitude')

figure
plot(Rbin, rawscansV, Rbin, bpfscansV, Rbin, mfscansV)
title('All Values'), xlabel('Meters'), ylabel('Amplitude')

Published with MATLAB® R2020a

Consider Appendix C of the MRM RET Users Guide. Determine the power in Watts at the transmit antenna port for a transmit gain setting of 63 and of 0.
When the gain is 63 the power is 2.1 for P400, -12.64 for P410, and 0.71 for P410 w Amps.
When the gain is 0 the power is -14.53 for P400, -31.6 for P410, and -12.48 for P410 w Amps.

In the MRMplotter.m code, explain how Rbin vector (the x-axis for your plots) was constructed. Where does Tbin come from? (Hint: see the MRM RET Users Guide)
First you create a vector ranging from 0 to the size of mfscanV-1. This is multiplied by Tbin. Then multiply by c and divide by 2 since the pulses go in multiple directions. Tbin is the threshold. The Threshold Multiple is the number of standard deviations that a received signal must deviate from nominal in order to generate a detection.